## Slide 1
Number systems and codes: Positional and non-positional number systems, Binary, Octal, Hexadecimal number system and conversion, Representation of negative and real numbers, Fixed and floating point numbers
Positional number system
Each symbol represents different value depending on its position in the number
Total value of a positional number is the total of the resultant value of all positions
Example: 12 = 1x101+2x100, 10+2 = 12
Non-positional number system
Each symbol represents the same value regardless of its position
Each symbol represents a number with its own place value
Example: Roman number system where I for 1, II for 2 etc.
Number system
Positional
Non-positional
Binary
Octal
Decimal
Hexadecimal
Binary number system is a base 2 number system having only 2 digits, 0 and 1 Example: 101101002
Octal number system is a base 8 number system having 8 digits, 0 to 7 Example: 17328
Decimal number system is a base 10 number system having 10 digits, from 0 to 9 Example: 324910
Hexadecimal number system is a base 16 number system having 16 digits, 0 to 9 similar to the decimal number system, A to F to represent 10 to 15 Example: A04B3C16

## Slide 2
Number conversion
1) Convert decimal 41 to binary
41
20
10
5
2
1
1
0
0
1
0
2
2
2
2
2
4110 = 1010012
1010012 = 1x25+0x24+1x23+0x22+0x21+1x20 =4110
2) Convert decimal 153 to octal
153
19
2
1
3
8
8
15310 = 2318
2318 = 2x82+3x81+1x80 = 15310
3) Convert decimal 0.6875 to binary
0.6875x2= 1.3750
0.3750x2= 0.7500
0.7500x2= 1.5000
0.5000x2= 1.0000
0.687510 = 0.10112
0.10112 = 1x2-1+0x2-2+1x2-3+1x2-4 = 0.687510
4) Convert decimal 0.513 to octal
0.513x8= 4.104
0.104x8= 0.832
0.832x8= 6.656
0.656x8= 5.248
0.248x8= 1.984
0.51310 = 0.406518
0.406518 = 4x8-1+0x8-2+6x8-3+5x8-4 +1x8-5 =0.51310
Convert decimal 41.6875 to binary
41.687510 = 101001.10112
Convert decimal 153.513 to octal
153.51310 = 231.406518

## Slide 3
5) 10 110 001 101 011.111 100 000 1102 = X8
X= 2 6 1 5 3.7 4 0 6
One octal digit corresponds to 3 binary digits
6) 10 1100 0110 1011.1111 00102 = X16
X= 2 C 6 B. F 2
One hexadecimal digit corresponds to 4 binary digits
7) 673.1248 = X2
X = 110 111 011 . 001 010 100
8) (306.D)16 = X2
X = 0011 0000 0110 . 1101
9) 39916 = X10
X = 3x162+9x161+9x160 = 921
10) 92110 = X16
921
57
3
16
16
9
9
X = 399
11) 0.51310 = X16
0.513x16 = 8.208
0.208x16=3.328
0.328x16=5.248
X = 0.835

## Slide 4
Representation of negative numbers
Sign magnitude representation → MSB represents sign of the number
01001 represents +9 for signed binary and 9 for unsigned binary
11001 represents -9 for signed binary and 25 for unsigned binary
Use to represent signed number in ordinary arithmetic
2) Signed complement representation
Use to implement arithmetic operation in computer
Negative number is implemented by its complement
Complement
Used in digital computer for simplifying subtraction operation
Radix complement = r’s complement
r’s complement of positive number N in base r with an integer part of n digits is rn – N for N≠0 and 0 for N=0
Example: 10’s complement of (52520)10 (here N=52520, r=10, n=5) = 105 – 52520 = 47480
(0.3267)10 (here N=.3267, r=10, n=0) = 100 – 0.3267 = 0.6733
(25.639)10 (here N=25.639, r=10, n=2) = 102 – 25.639 = 74.361
2’s complement of (101100)2 (here N=101100, r=2, n=6) = (26)10 – (101100)2 = (1000000-101100)2=010100
(0.0110)2 (here N=0.0110, r=2, n=0) = (20)10 – (0.0110)2 = (1- 0.0110)2=0.1010

## Slide 5
Diminished radix complement = (r-1)’s complement
(r-1)’s complement of positive number N in base r with an integer part of n digits and a fraction part of m digits is (rn – r-m)-N
Example: 9’s complement of (52520)10 (here N=52520, r=10, n=5, m=0) = 105 – 10-0-52520 = 47479
(0.3267)10 (here N=.3267, r=10, n=0, m=4) = 100 – 10-4-0.3267 = 0.6732
(25.639)10 (here N=25.639, r=10, n=2, m=3) = 102 – 10-3-25.639 = 74.360
1’s complement of (101100)2 (here N=101100, r=2, n=6, m=0) = (26 -20)10 – (101100)2 = (111111-101100)2=010011
(0.0110)2 (here N=0.0110, r=2, n=0, m=4) = (20 -2-4)10 – (0.0110)2 = (0.1111- 0.0110)2=0.1001
Representation of real number, fixed point number and floating point number
A set is a collection of objects, typically grouped within braces {}, where each object is called an element
For example, {red, green, blue} is a set of colours
A subset is a set consisting of elements that belong to a given set
For example, {green, blue} is a subset of the above colour set
A set with no elements is called the empty set and has its own special notation, {} or 
Set of natural numbers, denoted by N, → {1, 2, 3,4, 5, ….}
numbers continue without bound
Set of whole numbers, denoted by W, is the set of natural number combined with 0 → {0, 1, 2, 3, 4, 5,…..}
Set of integers, denoted by Z consists of both negative and positive whole numbers, as well as zero→{…,-3,-2, -1, 0, 1, 2, 3…}
Set of natural and whole numbers are both subsets of the set of integers

## Slide 6
Rational numbers, denoted by Q, are defined as any number of the form
Decimals that repeat or terminate are rational. For example, 0.7 =
The set of integers is a subset of the set of rational numbers because every integer can be expressed as a ratio of the integer and 1, can be considered as rational number. For example, 5 =
Irrational numbers, defined as any number that can not be written as a ratio of two integers
Nonterminating decimal, that do not repeat are irrational
For example,  = 3.14159…, 2 = 1.41421…
Real numbers, denoted by R, defined as the set of all rational numbers, combined with the set of all irrational numbers. All the numbers defined so far are the subsets of the set of real numbers.
Rational
Integers {…-2, -1, 0, 1, 2,…}
Whole {0, 1, 2, 3,…}
Natural {1, 2, 3,…}
Irrational 3, , 0.10010001…

## Slide 7
Storing real numbers
Unsigned integer
Signed integer
Unsigned fixed point
Signed fixed point
Floating point
Variable length
Unsigned rational
Signed rational
Integer
Sign Integer
Integer Fraction
Sign Integer Fraction
Sign Exponent Sign Mantissa
Sign Size Digits
Numerator Denominator
Sign Numerator Denominator
Two major approaches to store real numbers
Fixed point notation has a fixed number of digits after the decimal point
Floating point notation has a varying number of digits after the decimal point
Fixed point representation of a number has fixed number of bits for integer part and fractional part
Example, 32-bit format, 1 bit for sign, 15-bit for the integer part and 16-bit for the fractional part
1 000000000101011 1010000000000000
N= -43.625
→
Sign
Fractional part
Integer part
Disadvantage
Relatively limited range of values that they can represent
Inadequate for numerical analysis as it does not allow enough numbers and accuracy
A number whose representation exceeds 32-bit would have to be stored inexactly
0 000000000000000 0000000000000001
=2-16=0.000015 approximately
Largest positive number in 32-bit format
0 111111111111111 1111111111111111
Smallest positive number in 32-bit format
=215(1-2-16)
3
-3
3.5
-3.5

## Slide 8
Floating point representation
The range of numbers that can be represented by a fixed point number code is in sufficient for many applications, particularly scientific computations where very large or very small numbers are frequently encountered.
Scientific notation permits such number to be represented using relatively few digits.
For example, it is easier to write 1.0 x 1018 (scientific notation) than 1 000 000 000 000 000 000 (fixed point notation)
Three numbers are associated with floating point number, format M x BE
M = mantissa, B = base, E = exponent
The precision of M x BE is determined primarily by the number of digits used in M. The range is determined by B and E.
Floating point number representation is inherently redundant in the sense that the same number can be represented in more than one way.
For example, 1.0 x 1018 = 0.1 x 1019 = 1000000 x 1012 = 0.000001 x1024
Normalization is used to specify the floating point number in a unique normal form for computer implementation
The mantissa is said to be normalized if the digit to the right of the binary point is not 0 i.e. there is no leading 0’s in the magnitude part of the number.
So 0.1 x 1019 is the unique normal form for the number 1.0 x 1018.
Unnormalized floating point number is easily normalized by shifting the mantissa to the right or left and appropriately incrementing or decrementing the exponent

## Slide 9
Representation of 0 in floating point number system
M=0 but the exponent may have any value as 0 x BE = 0 for all values of E
Representation of very small number needs a very large negative exponent, say –K. For example, 0.1x10-56
If k bits are allowed for the exponent field including its sign then 2k exponent bit patterns are available to represent signed integers, which can range either from -2k-1 to 2k-1-1 or from -2k-1 +1 to 2k-1. So that K=2k-1 or 2k-1-1.
Floating point exponent be encoded in excess-K code where the exponent field contains an integer part that is the desired exponent value plus K. The quantity K is called bias and the exponent encoded in this way is called a biased exponent or characteristic.
Possible values of an 8-bit exponent with bias 127 (= (28-1-1)) and 128 (= 28-1)
Exponent bit pattern | Unsigned value E | Signed value E for K=127 (28-1-1) | Signed value E for K=128 (28-1)
11111111 11111110 . . . 10000001 10000000 01111111 01111110 . . . 00000001 00000000 | 255 254 . . . 129 128 127 126 . . . 1 0 | +128 +127 . . . +2 +1 0 -1 . . . -126 -127 | +127 +126 . . . +1 0 -1 -2 . . . -127 -128

## Slide 10
IEEE (Institute of Electrical and Electronics Engineers) 754: Standard format for 32-bit floating point number
32-bit floating point number: 1-bit for sign, 23-bit for mantissa and 8-bit for exponent
Sign
Mantissa part
Exponent part
Mantissa part of a normalized sign magnitude number always has 1 as its most significant digit
No need to store this 1 in floating point number , since it can always be inserted by the arithmetic circuit that processes the number
In 754 format complete mantissa = 1.M , N=0.1101111100000011111100110111 x234 = 1.101111100000011111100110111x233
Hidden leading bit 1 increases the precision
of a normalized number by 1
Exponent is represented in 8-bit excess-127 code.
Actual exponent = E-127
1-bit left shift (right shift) of M increases (decreases) exponent by 1
Real number represented by 32-bit floating point number in IEEE 754 standard is N = (-1)S2(E-127)(1.M) provided 0<E<255
i.e. 1≤ E≤ 254, minimum value of E is 1 and maximum value of E is 254 for valid floating point number
23-bit M
1.M

## Slide 11
Example: N = (-1)S2(E-127)(1.M)
1) N = -1.510 = -1.12 = -1.1x20 i.e. S=1, M=1 and desired exponent (E-127) = 0
01111111
1
10000000000000000000000
Sign bit is 1 as the number is negative
Exponent = 0, so E-127 = 0 and hence E=127
Smallest positive normalized floating point number in 32-bit format
Minimum E =1 and so E-127 = 1-127 = -126
M = 00000000000000000000000
N= (-1)S2(E-127)(1.M) = (-1)02(-126)(1. 00000000000000000000000)
Largest positive normalized floating point number in 32-bit format
Maximum E = 254 and so E-127 = 254 – 127 = 127
M = 11111111111111111111111
N= (-1)S2(E-127)(1.M) = (-1)02(127)(1. 11111111111111111111111) = (2-2-23)x2127

## Slide 12
Characteristic codes – ASCII, EBCDIC etc. and others like Gray, Excess-3 etc.
Computer codes are used for internal representation of data in computers
As computer uses binary numbers for internal data representation, computer codes use binary coding schemes
Binary code is represented by the number as well as alphanumeric letter
2
4
8+4+2+1
0010
Advantages of Binary code
Suitable for the computer applications and digital communications
Easy to implement as use only 0 and 1
Classification of binary codes
Weighted codes/Non-weighted codes
Binary coded decimal code
Alphanumeric codes
Non-weighted codes: In this type of binary codes, the positional weights are not assigned. Excess-3 code and Gray code are the examples of such code
8+4+2+1
0100
Decimal
Positional weights
Codes
Weighted codes: Weighted binary codes are those binary codes which obey the positional weight principle. Each position of the number represents a specific weight. Several systems of the codes are used to express the decimal digits 0 through 9. In these codes each decimal digit is represented by a group of four bits.

## Slide 13
Binary coded decimal (BCD)
Use to represent decimal digits. Each decimal digit is represented by a 4-bit binary number.
Using 4 bits we can represent sixteen numbers (0000 to 1111). But in BCD code only first ten of these (0000 to 1001) are used. The remaining six code combinations (1010 to 1111) are invalid in BCD.
Weights in the BCD codes are 8, 4, 2, 1
For example, 0110 = 0x8+1x4+1x2+0x1 = 6
Possible to assign negative weights to a decimal code, say, 8, 4, -2, -1
For example, 0110 = 0x8+1x4+1x-2+0x-1 = 2
2421 is another weighted code
For example, 0110 = 0x2+1x4+1x2+0x1 = 6
Advantages of BCD codes
Similar to decimal system
Need to remember binary equivalent of decimal numbers 0 through 9
Disadvantages of BCD codes
Addition and subtraction of BCD have different rules
BCD needs more number of bits than binary to represent the decimal number. So BCD is less efficient than binary.
For example, 11 in decimal = 1011 in binary = 0001 0001 in BCD
Excess-3 code
Used in old computers
Non-weighted code
Use to represent decimal number
Code assignment is obtained from the corresponding value of BCD after the addition of 3
Decimal digits | BCD 8421 | Excess-BCD+0011 | 84-2-1 | 2421
0 | 0000 | 0011 | 0000 | 0000
1 | 0001 | 0100 | 0111 | 0001
2 | 0010 | 0101 | 0110 | 0010
3 | 0011 | 0110 | 0101 | 0011
4 | 0100 | 0111 | 0100 | 0100
5 | 0101 | 1000 | 1011 | 1011
6 | 0110 | 1001 | 1010 | 1100
7 | 0111 | 1010 | 1001 | 1101
8 | 1000 | 1011 | 1000 | 1110
9 | 1001 | 1100 | 1111 | 1111

## Slide 14
Numbers are represented in digital computers either in binary or in decimal through a binary code
User likes to give data in decimal form, input decimal number is stored internally in the computer by means of a decimal code
Each decimal digit requires at least 4 binary storage elements
Decimal numbers are converted to binary when arithmetic operations are done internally with numbers represented in binary
Arithmetic operation can be performed directly in decimal with all numbers left in a coded form throughout
For example, the decimal number 395, when converted to binary, is equal to 110001011, having 9 binary digits
Same number 395 when represented internally in the BCD code, occupies 12 bits, 0011 1001 0101
Gray code | Decimal equivalent
0000 0001 0011 0010 0110 0111 0101 0100 1 100 1 101 1 111 1 110 1 010 1 011 1 001 1 000 | 0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
Gray code
Digital system can be designed to process data in discrete form only. Many physical systems supply continuous output data i.e. analog data. Such data must be converted into digital form before they are applied to a digital system.
It is sometimes convenient to use the gray code to represent the digital data when it is converted from analog data
Advantage of using gray code over binary code is that only 1 bit in the code group changes when going from one number to the next
Used in application where the normal sequence of binary numbers may produce an error or ambiguity during the transition from one number to the next
For example, a change from 0111 to 1000 may produce an intermediate erroneous number 1001 if the right most bit takes more time to change than the other 3 bits. In gray code only one bit changes in value during any transition between two numbers
Non-weighted code and can not be used for arithmetic operation

## Slide 15
Two bit gray code
00  0
01  1
11  2
10  3
Four bit gray code
0000  0
0001  1
0011  2
0010  3
0110  4
0111  5
0101  6
0100  7
1100  8
1101  9
1111  10
1110  11
1010  12
1011  13
1001  14
1000  15
Two bit binary code
00  0
01  1
10  2
11  3
Three bit binary code
000  0
001  1
010  2
011  3
100  4
101  5
110  6
111  7
Three bit gray code
000  0
001  1
011  2
010  3
110  4
111  5
101  6
100  7
Four bit binary code
0000  0
0001  1
0010  2
0011  3
0100  4
0101  5
0110  6
0111  7
1000  8
1001  9
1010  10
1011  11
1100  12
1101  13
1110  14
1111  15
00

## Slide 16
Alphanumeric codes
A binary digit or bit can represent only two symbols as it has only two states ‘0’or ‘1’’. But this is not enough for communication between two computers because there we need many more symbols for communication. These symbols are required to represent 26 alphabets with capital and small letters, numbers from 0 to 9, punctuation marks and other sysbols.
The alphanumeric codes are the codes that represent numbers and alphabetic characters. Mostly such codes also represent other characters such as symbol and various instructions necessary for conveying information. An alphanumeric code should at least represent 10 digits and 26 letters of alphabet i.e. total 36 items.
ASCII and EBCDIC
ASCII stands for the "American Standard Code for Information Interchange". It was designed in the early 60's, as a standard character set for computers and electronic devices. ASCII is a 7-bit character set containing 128 characters.
EBCDIC stands for Extended Binary Coded Decimal Interchange Code., Data-encoding system, developed by IBM, that uses a unique eight-bit binary code for each number and alphabetic character as well as punctuation marks and accented letters and non-alphabetic characters.