## Slide 1
Boolean function
An expression formed with binary variables, two binary operators OR and AND, unary
operator NOT, parentheses and equal sign
For a given value of the variables, function can be either 0 or 1
May also be represented in a truth table, number of rows in the truth table is 2n where n is the number of binary variables in the function
x | y | z | F1 | Minterms | Maxterms
0 | 0 | 0 | 0 |  | x+y+z
0 | 0 | 1 | 1 | xyz | 
0 | 1 | 0 | 0 |  | x+y+z
0 | 1 | 1 | 1 | xyz | 
1 | 0 | 0 | 0 |  | x+y+z
1 | 0 | 1 | 0 |  | x+y+z
1 | 1 | 0 | 1 | xyz | 
1 | 1 | 1 | 0 |  | x+y+z
In SOP form F1=xyz+xyz+xyz
In POS form F1=(x+y+z).(x+y+z).(x+y+z).(x+y+z).(x+y+z)
The Boolean function F1 can be expressed as sum of product (SOP) terms or as product of sum (POS) terms
Product terms (Minterms) are obtained from those rows of the truth table for which F1 is 1 and sum terms (Maxterms) are obtained from those rows of the truth table for which F1 is 0
Product terms
Sum terms

## Slide 2
xy+yz+(xyz) = xy+yz+x+y+z=y(1+x)+z(1+y)+x=x+y+z
z
y
x
xy
yz
(xyz)
x
y
z
Algebric manipulation
Literal is a primed or unprimed variable
Each literal in the Boolean function designates an input to a gate
Each term in the Boolean function is implemented with a gate
Minimization of the number of literals and number of terms reduces number of equipments in a circuit
Boolean function may be transformed from an algebric expression into a logic diagram composed of AND, OR, NOT gates

## Slide 3
Boolean algebra: Use to simplify the Boolean functions to minimum number of literals
Laws and theorems of Boolean algebra
Duality: (a) (i) x+x=x (ii) x+1=1 (iii) x+0=x (iv) x+x=1
(b) (i) x.x=x (ii) x.0=0 (iii) x.1=x (iv) x.x=0
Commutative law: (i) x+y=y+x (ii) x.y=y.x
Associative law: (i) x+(y+z)=(x+y)+z (ii) x.(y.z)=(x.y).z
Distributive law: (i) x+y.z=(x+y).(x+z) (ii) x.(y+z)=x.y+x.z
Involution: (x) = x
De-Morgans theorems: (i) (x+y)=xy (ii) (xy)=x+y
Absorption: (i) x+xy=x (ii) x.(x+y)=x
Operator precedence for evaluating boolean expression
(1) Parentheses (2) NOT (3) AND (4) OR
Example
(x+y) → Expression inside the parentheses is evaluated first and the result is then complemented
x. y → Complement of x and complement of y are evaluated first, the result is then ANDed
Ex. Simplify the following Boolean functions to minimum number of literals
1. x+x´y =(x+x´)(x+y) = 1.(x+y)=x+y
2. x(x´+y) = xx´+xy=0+xy=xy
3. x´y´z+x´yz+xy´=x´z(y´+y)+xy´=x´z+xy´
4. xy+x´z+yz = xy+x´z+yz(x+x´) = xy+x´z+xyz+x´yz = xy(1+z)+x´z(1+y) = xy+x´z

## Slide 4
5. F1=xyz+xyz+xyz =xz(y+y)+xyz = xz+xyz
6. F1=(x+y+z).(x+y+z).(x+y+z).(x+y+z).(x+y+z)=(x+z+yy).(x+y+zz).(x+y+z)
= (x+z).(x+y).(x+y+z) = (xx+zx+xy+yz).(x+y+z) = (0+ zx+xy+yz).(x+y+z)
= zx+xyx+yzx+zxy+xyy+yzy+zxz+xyz+yzz = zx+0+yzx+zxy+0+0+0+xyz+0
= zx(1+y+y)+xyz = zx(1+1)+xyz = zx+xyz
Universal logic gate: NAND and NOR are universal logic gate as all the other logic gates can be designed using NAND and NOR
AND by NAND: AB = ((AB))
A
B
OR by NAND: A+B = ((A+B)) = ((A).(B))
A
B
NOT by NAND:
A
A
A
B
A
B
(AB)
((A.B).(A.B))  XOR
XOR by NAND: A.B +A.B=((A.B +A.B ))= ((A.B).(A.B))
(A.(AB))=(A.(A+B))=(A.A+AB)
=(0+AB)=(AB)
(B.(AB))=(B.(A+B))=(B.A+BB)
=(AB+0)=(AB)
((A.B).(A.B))  XNOR
(A.A)=A

## Slide 5
AND by NOR: A.B = ((A.B))= ((A)+(B))
A
B
OR by NOR: A+B = ((A+B))
A
B
NOT by NOR:
A
A
((A)+(B))
A
B
((A+B))
(A+B)
B
XOR by NOR
(A+(A+B))=(A+A.B)=((A+A).(A+B))
=(1.(A+B))=(A+B)
(A+B)
(B+(A+B))=(B+A.B)=((B+A).(B+B))
=((B+A).1)=(B+A)
((B+A)+(A+B))=(A.B+AB)  XNOR
(A.B+AB)  XOR
A
Half adder (HA)
HA
A
B
Sum
Carry
Sum
B
A
A | B | Sum | Carry
0 0 1 1 | 0 1 0 1 | 0 1 1 0 | 0 0 0 1
Half adder has two inputs (A, B) and two outputs (Sum, Carry).
Sum = A.B+ A.B and Carry = A .B
So Sum is obtained from the output of XOR gate and Carry is obtained from the output of AND gate.
Carry
(A+A)=A

## Slide 6
FA
B
A
Sum
Carry
C
A
B
C
Carry
Sum
Full adder (FA) using logic gates
Sum1 and Carry1 are the outputs of HA1
Sum and Carry2 are the outputs of HA2
Sum and Carry are the outputs of FA
Carry1
Sum1
Carry2
HA1
Carry
Carry1
HA2
Sum
Carry2
OR
Full adder (FA): Full adder has three inputs (A, B, C) and two outputs (Sum, Carry).
A
C
B
Full adder (FA) using two half adders
A | B | C | Sum | Minterms | Maxterms | Carry | Minterms | Maxterms
0 0 0 0 1 1 1 1 | 0 0 1 1 0 0 1 1 | 0 1 0 1 0 1 0 1 | 0 1 1 0 1 0 0 1 | ABC ABC ABC ABC | A+B+C A+B +C A +B+C A +B+C | 0 0 0 1 0 1 1 1 | ABC ABC ABC ABC | A+B+C A+B+C A+B+C A+B+C
Sum=ABC+ABC+ABC +ABC in SOP
Sum = (A+B+C).(A+B+C).(A+B+C).(A+B+C) in POS
Carry=ABC+ABC+ABC+ABC in SOP
Carry = (A+B+C).(A+B+C).(A+B+C).(A+B+C) in POS
Sum1

## Slide 7
Simplify Sum and Carry
Sum=ABC+ABC+ABC +ABC=A(BC+BC)+A(BC+BC)=A(BC+BC )+
A(BC+BC)=A(B xor C)+A(B xor C)=A xor B xor C
Sum = (A+B+C).(A+B+C).(A+B+C).(A+B+C)
= (A.A+A.B+A.C+AB+BB+CB+AC+BC+CC).(AA+AB+AC+AB+BB+C B+
AC+BC+CC)
= (A+AB+AC+AB+0+CB+AC+BC+0).(A+AB+AC+AB+0+CB+AC+BC+0)
= (A.(1+B+C+B+C)+BC+BC).(A.(1+B+C+B+C)+BC+BC)
= (A+BC+BC).(A+BC+BC) = AA+ABC+ABC+ABC+ABC
= ABC+ABC+ABC+ABC = A xor B xor C
Carry=ABC+ABC+ABC+ABC=BC(A+A)+ABC+ABC=BC+ABC+ABC
=C(B+AB)+ABC=C(B+A)(B+B)+ABC=BC+AC+ABC=B(C+AC)+AC
=B(C+A)(C+C)+AC=AB+BC+CA
Carry = (A+B+C).(A+B+C).(A+B+C).(A+B+C)
= (A+B+CC).(AA+AB+AC+AB+BB+BC+AC+BC+CC)
= (A+B).(0+AB+AC+AB+0+BC+AC+BC+C)
= (A+B).(C(1+B+A+B+A)+AB+AB) = (A+B).(C+ AB+AB) = AC+BC+AAB+BAB+AAB+BAB=AC+BC+AB+AB+0+0=AC+BC+AB